How to use the ESFT radio system:

DO NOT UPDATE THE SYSTEM PACKAGES IT WILL BREAK THINGS

1. Make sure all connections are solid.
☐ The LimeSDR is plugged into the Raspberry Pi
☐ The BladeRF is plugged into the basestation computer
☐ The antenna on the BladeRF is on the RX connector
☐ The antenna on the LimeSDR is on the TX connector

2. Connect the flight computer to a local DHCP Server
☐ The flight computer should be connected to Wifi
☐ The flight computer should have an IP address

3. Establish an SSH connection to the flight computer and open a terminal
☐ The flight computer is remotely controllable

4. At the base station, set up the receiver system
☐ Launch the bladereceiver.py from the /Documents/gnuradio/ folder
☐ Launch the decoder terminal from the /Documents/esft/ folder

5. Create the TMUX sessions with the following commands:
- “tmux new -s encoder”
- “cd datafiles”
- “sudo ./encoder”
then press CTRL + B then D to exit

- “tmux new -s transmitter”
- “cd pythonscripts”
- “sudo ./plutotransmitter”
then press CTRL + B then D to exit

☐ The encoding and transmitting software is running

6. Ensure the system is operational
☐ The waveform is continous
☐ The transmitter can be stopped and started at will without crashing
☐ The encoder correctly encodes data from sensor input
☐ The decoder displays all information correctly and records it to a file

At the end of flight shutdown flight computer properly with “sudo shutdown now”